## Slide 1: Homework 3 explanation
NCKU CSIE DICLAB

## Slide 2: Introduction
Design an circuit with addition, subtraction, and multiplication functions
The input only consists of numbers 0 to 15, four operators: +, -, *, =, and paratheses
The inputs are represented in ASCII codes
The input expression string will not exceed 16 characters
It’s difficult for computers to comprehensively process and handle the entire equation
  Converting the notation of the expression from infix to postfix

## Slide 3: Finite State Machine
BUFFER：Read input string and store it into buffer
IN2POS：Convert the input string to postfix
POP：Pop out remaining operators in the buffer
CALCULATE：Calculate results according to the postfix expression
RESULT：Pull up ‘valid’ signal and output calculation result
RESET：Pull down ‘valid’ signal and go back to ‘BUFFER’ state

## Slide 4: Data Registers
dataBuffer: used to store input string
OpStack: store operators while converting expression to postfix
OutBuffer: store converted postfix output string
sum: buffer for calculation

## Slide 5: BUFFER
Decode ASCII code to numbers
  The codes for operators are directly stored into ‘dataBuffer’

## Slide 6: IN2POS
arrPt：index used to scan ‘dataBuffer’
stackPt：index of ‘OpStack’
If the current token of ‘dataBuffer’ is 40 (‘(’), push it to ‘OpStack’
  Store the value of ‘dataBuffer[arrPt]’ to OpStack[stackPt]
  Increase the value of ‘stackPt’ by 1 (Push operation)
  Increase the value of ‘arrPt’ by 1 (Scan the next token)

## Slide 7: IN2POS
If the current token of ‘dataBuffer’ is 41 (‘)’), pop tokens from ‘OpStack’ until a left parenthesis is found
  If the top token of ‘OpStack’ is not parenthesis, pop out it from stack and append it to output string
    Line 91 & 92: append a value to ‘OutBuffer’ and increase its index (outPt) by 1
  No matter whether the top token of ‘OpStack’ is a left parenthesis, it should be popped out (Line 94)
  If the top token of ‘OpStack’ is a left parenthesis, scan the next token from the input string (Line 95)

## Slide 8: IN2POS
If the current token of ‘dataBuffer’ is 42 (‘*’), pop tokens from ‘OpStack’ until the precedence of the top token is lower than that of the current token
  If the top token of ‘OpStack’ is ‘*’, pop out the top token and append it to the output string (Line 98 ~ 102)
  Otherwise, push the current token onto ‘OpStack’ (Line 103 ~ 107), and scan the next token from the input string (Line 106)

## Slide 9: IN2POS
If the current token of ‘dataBuffer’ is 43 or 45 (‘+’ or ‘-’), pop tokens from ‘OpStack’ until the precedence of the top token is lower than that of the current token
  If the top token of ‘OpStack’ is ‘+’、 ‘-’ 、‘*’, pop out the top token and append it to the output string (Line 110 ~ 114)
  Otherwise, push the current token onto ‘OpStack’ (Line 115 ~ 119), and scan the next token from the input string (Line 118)
  The pop operation will stop only when a left parenthesis is found or the stack becomes empty

## Slide 10: IN2POS
If the current token of ‘dataBuffer’ is a number (0~15), append it to the output string

## Slide 11: POP
If ‘OpStack’ has remaining tokens, pop them out append them to the output string
  Line 129：Judge if ‘OpStack’ is empty
  Line 130：Pop operation
  Line 131：Ignore parenthesis while appending
  Line 132 & 133：append the top token of ‘OpStack’ to ‘OutBuffer’, and increase the index of ‘OutBuffer’ by 1

## Slide 12: CALCULATE
Use stack ‘sum’ for calculation
  If the current token of ‘OutBuffer’ is a number, push it onto the stack (Line 152 ~ 155)
  Otherwise, pop out two tokens from the stack and calculate, store the calculation results back into the stack (Line 140 ~ 151)

## Slide 13: RESULT & RESET
Pull up the ‘valid’ signal (Line 159), and reset registers (Line 160 ~ 172)
Pull down the ‘valid’ signal at the next cycle (Line 175)

## Slide 14: Example
Given an expression in infix notation “3 + 4 * (2 - 1)”, convert it to postfix and calculate the result
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 15: Example
dataBuffer[0] = 3, append it to the output string (Line 121 ~ 125)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 16: Example
dataBuffer[1] = ‘+’. ‘OpStack’ is empty, push ‘+’ onto ‘Opstack’ (Line 115 ~ 119)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 17: Example
dataBuffer[2] = 4, append it to the output string (Line 121 ~ 125)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 18: Example
dataBuffer[3] = ‘*’, the precedence of the top token of ‘OpStack’ is lower, push ‘*’ onto ‘OpStack’ (Line 103 ~ 107)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + | * |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 19: Example
dataBuffer[4] = ‘(’, push it onto ‘OpStack’ (Line 84~88)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + | * | ( |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 20: Example
dataBuffer[5] = 2, append it to the output string (Line 121 ~ 125)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + | * | ( |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 21: Example
dataBuffer[6] = ‘-’, the top token of ‘OpStack’ is a left parenthesis, push ‘-’ onto ‘OpStack’ (Line 115 ~ 119)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + | * | ( | - |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 22: Example
dataBuffer[7] = 1, append it to the output string (Line 121 ~ 125)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + | * | ( | - |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 |  |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 23: Example
dataBuffer[8] = ‘)’, the top token of ‘OpStack is ‘-’, pop ‘-’ from ‘OpStack’ and append it to the output string (Line 90 ~ 94). ‘arrPt’ = len – 1, next state is ‘POP’
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + | * | ( |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 24: Example
stackPt != 0, pop a token from OpStack (Line 130). The token is ‘(’, so it will not be append to the output string. (Line 131)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + | * |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - |  |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 25: Example
stackPt != 0, pop a token from OpStack (Line 130). The token is ‘*’, so it will be append to the output string. (Line 132 ~ 133)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | + |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * |  |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 26: Example
stackPt != 0, pop a token from OpStack (Line 130). The token is ‘+’, so it will be append to the output string. (Line 132 ~ 133)
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 27: Example
stackPt = 0, no operation. Next state is ‘CALCULATE’
arrPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | + | 4 | * | ( | 2 | - | 1 | ) |  |  |  |  |  |  | 
dataBuffer
len = 9
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OpStack
outPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer

## Slide 28: Example
‘StackPt’ is used as index for scanning ‘OutBuffer’, increase ‘stackPt’ by 1 (Line 138)
OutBuffer[0] = 3, push it onto ‘sum’ (Line 152 ~ 155)
outPt = 7
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sum

## Slide 29: Example
‘StackPt’ is used as index for scanning ‘OutBuffer’, increase ‘stackPt’ by 1 (Line 138)
OutBuffer[1] = 4, push it onto ‘sum’ (Line 152 ~ 155)
outPt = 7
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sum

## Slide 30: Example
‘StackPt’ is used as index for scanning ‘OutBuffer’, increase ‘stackPt’ by 1 (Line 138)
OutBuffer[2] = 2, push it onto ‘sum’ (Line 152 ~ 155)
outPt = 7
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
sum

## Slide 31: Example
‘StackPt’ is used as index for scanning ‘OutBuffer’, increase ‘stackPt’ by 1 (Line 138)
OutBuffer[3] = 1, push it onto ‘sum’ (Line 152 ~ 155)
outPt = 7
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 |  |  |  |  |  |  |  |  |  |  |  | 
sum

## Slide 32: Example
‘StackPt’ is used as index for scanning ‘OutBuffer’, increase ‘stackPt’ by 1 (Line 138)
OutBuffer[4] = ‘-’
  Pop sum[2] and sum[3], push sum[2] – sum[3] back to ‘sum’ (Line 149)
  Decrease sumPt by 1 (Line 150)
outPt = 7
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
sum

## Slide 33: Example
‘StackPt’ is used as index for scanning ‘OutBuffer’, increase ‘stackPt’ by 1 (Line 138)
OutBuffer[5] = ‘*’
  Pop sum[1] and sum[2], push sum[1] * sum[2] back to ‘sum’ (Line 141)
  Decrease sumPt by 1 (Line 142)
outPt = 7
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sum

## Slide 34: Example
‘StackPt’ is used as index for scanning ‘OutBuffer’, increase ‘stackPt’ by 1 (Line 138)
OutBuffer[6] = ‘+’
  Pop sum[0] and sum[1], push sum[0] + sum[1] back to ‘sum’ (Line 145)
  Decrease sumPt by 1 (Line 146)
stackPt = outPt – 1 (before positive edge of ‘clk’), next state is ‘RESULT’
outPt = 7
stackPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 3 | 4 | 2 | 1 | - | * | + |  |  |  |  |  |  |  |  | 
OutBuffer
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sum

## Slide 35: Example
In ‘RESULT’ state
  Pull up ‘valid’ signal (Line 159)
  Result is sum[0] (Line 160)
  Initialized registers (Line 161 ~ 172)
sumPt = 1
sumPt | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
data | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sum